## Slide 1
Lecture 8
Rectal Dosage Forms
-2-

## Slide 2
Some examples of Synthetic bases:
witepsol: suppository base containing neutral fatty substances, mainly saturated fatty acid triglycerides.
There are four types:
Witepsol H (e.g.H12, H15, H19): low % of mono TG., Hydroxyl No. is low (3- 15), low melting range (32- 33.5 ◦C), narrow fusion range, suitable for hydrolyses -sensitive drugs, thermolabile drugs
Witepsol W (e.g. w35): wide fusion range, good viscosity, Hydroxyl No. is higher (20- 50),
Witepsol S (e.g. S55, S58): higher viscosity, contains surfactants, Hydroxyl No. is higher (50- 70), suitable for heavy suspended drugs,
Witepsol E (e.g. E75, E76, E85): high melting range (37- 44 ◦C), suitable for lipid soluble drugs (affect melting point), Hydroxyl No. is low (<15)

## Slide 3
<number>
PREPARATION OF SUPPOSITORIES
As we mentioned in the last lecture, Suppositories are prepared by one of three methods:
A- Fusion Molding
B- Compression Molding
C- Hand Rolling and Shaping

## Slide 4
<number>
A- Fusion Molding
It is the most commonly used method for producing suppositories on both a small and large scale.
The steps in molding process include:
melting the base
incorporating required medicaments
pouring the melt into moulds
allowing the melt to cool and congeal into suppositories and removing the formed suppositories from the mold.

## Slide 5
<number>
The molds are made from stainless steel, aluminum, brass, and plastic.
Molds are of various capacities, depending upon the scale of production.
In lab., there are molds capable of producing 6 to 12 suppositories.
Molds are opened longitudinally for cleaning before and after preparation of suppositories.
Brass: type of metal mixture of metals which consists of zinc and copper
Longitudinally: adv. in a longitudinal direction, lengthwise

## Slide 6
<number>

## Slide 7
<number>
A suppository mold with a capacity of 50 suppositories

## Slide 8
<number>

## Slide 9
<number>

## Slide 10
<number>

## Slide 11
<number>
This is an important step in the preparation of suppositories.
Lubrication is required for clean and easy removal of suppositories.
Lubrication is necessary when glycerinated gelatin suppositories are prepared.
A thin coating of mineral oil is applied to the molding surface, which provides sufficient lubrication.
Lubrication of the Mold

## Slide 12
<number>
When you prepare suppositories, It is necessary to account for different densities of different bases (e.g. the weight of suppositories prepared from cocoa butter base differs from that of PEG base for a particular mould. Furthermore, any added medicinal agent alters the density and hence the weight of the resulting suppository).
Calibration of the Mold

## Slide 13
<number>
Empty suppositories are prepared from base material alone.
Then, the suppositories are weighed and their volume is determined by melting.
Thus the density is calculated for that particular base.
In the case of extemporaneous preparations, the pharmacist needs to determine the amount of the base required to be incorporated together with the medicaments, so that each suppository provides the required amount of the drug.
The volume of the base required is determined by subtracting the volume of the medicaments from the total volume of the mold. Suppository bases are solids at room temperature, so the density of the material is used to calculate the volume of the base required
Mold Calibration method

## Slide 14
<number>
for example:
If 12 ml of cocoa butter is required to fill a mold of 6 supp.,
and if the volume of the medicaments is 3.4 ml,
then the volume of the cocoa butter required is 8.6 ml.
The weight of the base required is then obtained by multiplying the density of cocoa butter (d= 0.86 g/ml) x volume (V= 8.6 ml), and this equal to 7.4 g.
(W =dx V = 0.86 x 8.6 = 7.4 gr)
Mold Calibration method

## Slide 15
<number>
DENSITY (Dose Displacement) CALCULATIONS
when we use material with various densities, the weight of fixed volume is variable. Thus, it is important to know the density of the incorporated materials, to determine the weight of the individual suppositories.
This is generally based on a 2 g suppository weight and the quantity of the active ingredients is more than 100 mg.
(It is usually assumed that the volume occupied by the active drug is not significant and need not to be considered if its quantity is less than 100 mg or if a suppository weighs less than 2 g).

## Slide 16
<number>
To determine the weights of the base needed, the pharmacists should know the density factors of various bases and drugs. The density factors of cocoa butter are known.
There are two ways to calculate the weight of the base needed:
1- Density of drug and base are known:
M= n. Wsupp – (n.dd/db)
n: no. of supp.
W: weight of supp.
dd: drug density
db: base density

## Slide 17
2- dose replacement factor is known
M =Q – (f.s1 + f2.s2+…)
M: is the amount (g )of required base to prepare the supp.
Q: weight (g) of base in the mold without drug.
f: dose replacement factor
s: drug amount (g) in the supp.

## Slide 18
<number>
Dosage replacement factor calculation
f = Wb/Wd
Wb: weight of the replaced base in the mold
Wd: weight of the drug material in the supp in the mold.

## Slide 19
<number>

## Slide 20
<number>
In The lab.:
The weighed base is melted over a water bath by using the least possible heat (a porcelain casserole is generally used).
Medicaments are usually incorporated into a portion of the melted base by mixing.
This material is then added with stirring to the remaining base, which is cooled almost to its congealing point
This material is now poured carefully and continuously into the chilled mold (The chilled mold avoids settling of the solids within the mold and also aids in congealing)
Then, the mold is usually kept in the freezer to promote hardening of the suppositories.
When the suppositories are hard, the mold is removed from the freezer, the sections of the mold are separated, and the suppositories are removed, with pressure being exerted at the ends.
Preparing and Pouring the Melt
Casserole: A small round dish with a handle, usually of porcelain

## Slide 21
<number>
Be careful:
If the melt is not at the congealing point when poured into the cavities, the solids may settle within each cavity of the mold; this will cause inaccurate distribution of the active ingredient in the bulk of the suppository.
If any undissolved solid materials with a tendency to settle are present, the material should be poured with constant stirring.
Any volatile or thermolabile substances should be added to the base with comprehensive stirring at the congealing point.
Filling of the suppository cavity should be continuous to avoid layering, which may lead to a product that is easily broken when handled.
To ensure complete filling of the mold upon congealing, the melt is poured above the level of the mold over each opening. The excessive material prevents the formation of recesses (set back from the surface ) at the ends of the suppositories. After solidification the excess material is scrapped off smoothly with a spatula.
Preparing and Pouring the Melt

## Slide 22
<number>
In Industry:
Industrial preparation of suppositories on a large scale involves steps similar to those discussed above. However, it also involves automation for each of the basic processes such as pouring the melt into molds, refrigeration, and removal of suppositories from the mold.
The automatic molding machine is one in which all filling, ejecting, and mold-cleaning operations are fully automated (e.g. rotary machine)
The output of a typical rotary machine ranges from 3500 to 6000 suppositories an hour. In this machine, the chrome-plated brass molds are installed radially (in the form of rays) in the cooling turntable (rotating platform).
Preparing and Pouring the Melt

## Slide 23
<number>
(1) feeding device and filling hopper, (2) rotating cooling turntable, (3) suppository ejection station, (4) scraping device, (5) refrigerant inlet-outlet, (6) suppository
Automated rotary machine for large scale production of suppositories consists of:

## Slide 24
<number>
1-The prepared mass is fed into the filling hopper, where it is continuously mixed and maintained at constant temperature.

## Slide 25
<number>

## Slide 26
<number>
2- The suppository mold is lubricated by brushing or spraying and then filled to slight excess.
3- After the mass solidifies in the molds, the excess material is collected for use again (The cooling cycle is adjusted, as required by adjusting the speed of the rotary cooling turntable).

## Slide 27
<number>
4-The solidified suppositories are then taken to the ejecting station, where the mold is opened and the suppositories are pushed out by steel rods. The empty mold then proceeds for the repeating of the cycle.

## Slide 28
<number>
Please note:
The inner surface of the molds must be kept clean in order to prevent improper closing during production.
Incomplete closing of the molds results in rough suppositories with mold marks.
To ensure smooth and uniform final product, air jets are installed in the machine. They routinely clean the molds by blowing out any particles sticking to the inside of the mold at the end of each cycle.
Jet: stream of liquid or gas forced out of an opening

## Slide 29
B- COMPRESSION
This is an alternative method of preparing suppositories is by forcing the mixture of the suppository base and the medicaments into special molds using suppository making machines.
It is especially useful for making suppositories containing drugs that are thermolabile and for those containing substances that are insoluble in the base (where there is no chance of settling of insoluble matter during preparation as in the case of preparation by melting).
The limitation of this method is that it requires a special suppository machine.

## Slide 30
<number>
1- The suppository base and the medicaments are combined by complete mixing, and the heat produced by the friction of the process causes the base to soften into a paste (Mortar and pestle are used on a small scale, and on a large scale mechanically operated kneading mixers and warmed vessels are employed).
2- The suppository mass is filled into a cylinder, which is then closed, and the mass is forced out the other end by applying pressure mechanically or by turning a wheel.
Friction: n. abrasion, scraping; conflict
Pestle: muller, stick used for grinding with a mortar
Kneading: n. act of squeezing and shaping
Knead: v. squeeze, shape, blend

## Slide 31
<number>
3- After the die is filled completely, the movable end plate at the back of the die is removed and pressure is applied to the mass in the cylinder to collect the formed suppositories.

## Slide 32
<number>
C- HAND ROLLING AND SHAPING
This is a historic part of the art of the pharmacist and hence this method will be discussed shortly.
A cocoa butter base is employed in this method

## Slide 33
<number>
1- A plastic-like mass is formed from the base of grated cocoa butter and other ingredients by severe trituration.
2-The mass is rolled into a ball with the hands.
(Since the suppository base melts near body temperature, before handling it, hands need to be cooled below body temperature by dipping them in ice water).
Trituration: n. grinding into powder

## Slide 34
<number>
3- The mass is shaped into a cylinder with the help of the spatula.
4- The cylinder is cut into appropriate lengths with a knife, each length equal to one suppository.
5-The final shaping of the suppository is done with the fingertips. Alternatively, the cylindrical base can be pushed into a mould to give the suppositories a final uniform shape.

## Slide 35
<number>
Packaging, Storage and Handling
Glyceninated gelatin suppositories are usually packaged in well-closed screw-capped glass containers, preferably at a temperature below 35°C.
Cocoa butter–based suppositories are usually packaged by wrapping them individually into partitioned boxes to prevent contact and adhesion.

## Slide 36
<number>
Suppositories containing light-sensitive drugs are generally wrapped in an opaque material such as a metallic foil. Most commercially available suppositories are individually wrapped in either foil or polyvinyl chloride (PVC)-polyethylene.
Wrapped: adj. packed; bound; covered; enveloped; enclosed
Opaque: adj. not transparent, prevent the passage of light or radiation; dull

## Slide 37
<number>
Some suppositories utilize strip-packaging, with individual suppositories being separated by tearing along perforations located between suppositories.
Tearing: n. ripping, rending
Perforation: n. puncturing, making holes

## Slide 40
<number>
Since suppositories are sensitive to heat, they should be stored in a cool place, but they should not be frozen.
Cocoa butter suppositories must be stored below 30°C, preferably in a refrigerator (2 to 8°C).
Glycerinated gelatin suppositories should be stored below 35°C and can be stored at controlled room temperature (20 to 25°C).
Polyethylene glycol–based suppositories can be stored at usual room temperatures.

## Slide 41
<number>
Suppositories are adversely affected by humidity. High humidity causes them to become spongy, whereas an extreme dry environment results in the loss of moisture from suppositories, which makes them brittle.
Spongy adj. soft and porous, absorbent and elastic; be similar to a sponge

## Slide 42
<number>
Quality control of suppositories
Finished suppositories are routinely examined for their appearance. Several tests are performed on the finished suppositories to ensure their quality.

## Slide 43
<number>
Control parameters of suppositories:
appearance
weight
disintegration test
The softening (lequification) time test
The breaking test
content of active ingredient
drug release test (Dissolution test)

## Slide 44
<number>
The appearance of a suppository includes its odour, colour, surface condition and shape. These are organoleptically controlled.
The requirements for weight and disintegration are given in the European and national Pharmacopoeias.

## Slide 45
Uniformity of Weight (Mass)
(Ph. Eur. method 2.9.5)
Weigh individually 20 units taken at random, and determine the average mass.
- Not more than 2 of the individual masses deviate from the average mass by more than the percentage deviation (5%) shown in Table 2.9.5.-1 and none deviates by more than twice that percentage.

## Slide 46
<number>

## Slide 47
<number>
Disintegration Test for Suppositories (BP. 2007)
(Appendix XII C includes the requirements of Ph. Eur. method 2.9.2)
The test for disintegration of suppositories determines whether suppositories disintegrate or soften within a prescribed time when placed in a liquid medium under the prescribed experimental conditions.

## Slide 48
<number>
Disintegration occurs in not more than 30 minutes for fat-based suppositories and in not more than 60 minutes for water-soluble suppositories, unless otherwise justified and authorised.
The melting and dissolution behaviour is in fact reflected in the disintegration test.

## Slide 49
<number>
The softening time test:
It determines the liquefaction time of the suppository when immersed in a 37°C water bath (that simulates in vivo conditions).
The apparatus used appears in the next slide.
It consists of a cellophane tube is tied to both ends of a condenser. Water (37°C) is circulated through the condenser. The suppository is dropped into the tube and sits at the level shown in the above Figure.
The time it takes the suppository to melt completely in the tube is measured.
Liquefaction: process of causing to become liquid, transformation into a liquid

## Slide 50
Apparatus for measuring the liquefaction time of rectal suppositories (Setnikar apparatus)
Suppository
Cellophane
Tube

## Slide 51
<number>
The breaking test
It is designed to measure the fragility of suppositories.
Suppositories with different shapes have different breaking points.
The desired breaking point of differently shaped suppositories is set as the level at which the suppository withstands the break forces induced by all kinds of handling such as production, packaging, shipping, and patient in-use handling.
This can be tested in several ways including a tablet-crushing strength tester.

## Slide 52
<number>
Drug release from suppositories
This is the most important thing to realize for the patient because it is the determining step towards the success of the therapy.
Because there are very few ways to obtain in- vivo release information this will usually have to be explained from in-vitro release.

## Slide 53
Drug assay:
Drug is extracted from the dosage form and assayed qualitatively and quantitatively using appropriate analytical methods.

## Slide 54
<number>
DRUG INCOMPATIBILITIES AND STABILITY
The active ingredients must be compatible with the suppository base. A wide range of ingredients are incompatible with polyethylene glycol bases, including benzocaine, iodochlorhydroxyquin, sulfonamides, aspirin, silver salts, and tannic acid. Other materials, such as sodium barbital, salicylic acid, and camphor, tend to crystallize out of (outside of) polyethylene glycol bases.

## Slide 55
<number>
The completed products are generally considered dry or nonaqueous and thus provide a stable dosage form as long as they are protected from moisture and heat. The major indication of instability in suppositories is excessive softening. Sometimes suppositories may dry out, harden, or shrivel.
Nonaqueous: adj. not watery, not containing water.
Shrivel: v. shrink and dry up, decline, decrease in strength or intensity

## Slide 56
Rectal formulations other than suppositories
Apart from suppositories, many formulations can be used for the rectal administration of drugs.
For the treatment of local disturbances, such as hemorrhoids, fatty ointments are widely used.
In the treatment of rectocolitis large-volume enemas are used, e.g. 100 ml. This enables the drug to reach the upper part of the rectum and the sigmoid colon.
apart from: besides, except for, in addition to
Rectocolitis: inflammation of the last part of the colon

## Slide 57
<number>
For the systemic administration of drugs, delivery forms such as tablets, capsules and microenemas are used.
Tablets are not very attractive because they can not disintegrate rapidly, owing to the small amount of water present in the rectum

## Slide 58
<number>
Capsules used to achieve a systemic effect are usually filled with a solution or suspension of the drug in vegetable oil or paraffin. Such capsules are mostly of the soft-shell type. Limited experience has been obtained with this dosage form, but it seems that there are no striking differences between the bioavailability from rectal capsules and that from fatty suppositories.

## Slide 59
<number>
Microenemas are solutions or dispersions of the drug in a small volume (approximately 3 ml) of water or vegetable oil. This form is supplied in a small plastic container equipped (provided) with an application tube.

## Slide 60
After insertion of the tube, the container is emptied by compression the bulb. The advantage of this delivery system is that no melting and dissolution process is necessary before drug release can start, if water is used as a vehicle.

## Slide 62
Many solutions are administered rectally for local effects (e.g., hydrocortisone) or for systemic absorption (e.g., aminophylline). In the case of aminophylline, the rectal route of administration minimizes the undesirable gastrointestinal reactions associated with oral therapy.
Retention Enemas

## Slide 63
Corticosteroids are administered as retention enemas as secondary treatment of some patients with ulcerative colitis. Oil retention enemas serve to lubricate the rectum and lower bowel and soften the stool. Salad oil and liquid petrolatum are commonly used at a temperature of (32.8°C)
ulcerative colitis: repeated condition characterized by ulcers and severe irritation of the colon and rectum (causes bloody stools, hemorrhoids, and abdominal pain

## Slide 64
May be given for the following purposes:
To remove feces when an individual is constipated.
2. To remove feces and cleanse the rectum in preparation for an examination.
3. To remove feces prior to a surgical procedure to prevent contamination of the surgical area.
4. To administer drugs or anesthetic agents.
Evacuation Enemas

## Slide 65
They act by stimulation of bowel activity through irritation of the lower bowel and by distention (swelling, expanding ) with the volume of fluid instilled. When the enema is administered, the individual should be lying on the left side, which places the sigmoid colon (lower portion of the bowel) below the rectum and facilitates infusion of fluid. The length of time it takes to administer an enema depends on the amount of fluid to be infused.

## Slide 66
Precautions and requirements for enemas:
1. The rectal tube used for infusion of the enema solution should be smooth and flexible to decrease the possibility of damage to the mucous membrane that covers the rectum.
2. Tap water is commonly used for adults but should not be used for infants because of the danger of electrolyte imbalance.

## Slide 67
3. The colon absorbs water, and repeated tap water enemas can cause cardiovascular overload and electrolyte imbalance.
4. Repeated saline enemas can cause increased absorption of fluid and electrolytes into the bloodstream, resulting in overload.

## Slide 68
<number>
Many good results have been obtained with drugs delivered in microenemas, but this form is still of limited applicability because of its relatively high cost compared to suppositories. Moreover, administration cannot be performed easily by patients themselves, and it is rather difficult to deliver the total content of the plastic container.

## Slide 69
<number>
RECTAL OINTMENTS
Rectal ointments are primarily used for local action. Ointments are inserted into the rectum with the help of an insertion and delivery tip. After placement of the rectal tip on the ointment tube, the tip is slowly and carefully inserted into the anus. The ointment tube is depressed to release the medication through the rectal tip and into the anal canal.

## Slide 70
<number>
After use the rectal tip should be thoroughly cleaned and the ointment tube cap must be replaced. While selecting an ointment for rectal use, close attention should be given to the product formulation base. Water-soluble bases are easier to clean from applicator tips than oleaginous bases. The commonly used rectal ointments are benzocaine ointment (USP), and dibucaine ointment (USP)

## Slide 71
<number>
Controlled-release formulations
Controlled-release formulations are designed to release the active agent in a sustained and controlled fashion.
They have been the subject of considerable research but have yet to make a significant effect.
Hydrogels have been shown in human clinical studies to provide an acceptable polymeric system for rate-controlled delivery of antipyrine (fever reducing medicine ) and theophylline.

## Slide 72
<number>
Rate-controlled osmotic delivery systems have also proven useful in clinical studies in effecting systemic drug delivery comparable to that of intravenous administration for well absorbed drugs.
Since the total acceptable size of a rectal formulation significantly exceeds the size possible for oral formulations, rectal administration for the purposes of controlled-release offers a significant advantage.

## Slide 73
<number>
A major limiting factor is, however, the need to incorporate controlling agents designed to regulate drug release which would significantly
increase the total size of the dosage form. Since adult rectal dosage forms are acceptable up to 2.5 g, the total drug load which can be formulated in a rectal controlled-release formulation can be 2–3 times that possible in an oral formulation.

## Slide 74
For some therapeutic agents, this higher drug load can offer an advantage which is not achievable via the oral route. Development and marketing of rectal controlled-release formulations will, however, still be disadvantaged because of the perceived reluctance of patients to employ this route and problems of poor patient compliance.
Reluctance: n. unwillingness, hesitance

## Slide 75: End of Lecture 8